## Slide 1
The NGS Toolbox: Do I Need a Screwdriver or a Hammer?
nathan grubaugh

## Slide 2
Viral RNA
Host RNA
Host DNA
Total Nucleic Acid

## Slide 3
Illumina
Nanopore
Ion
Pacbio
BGI

## Slide 4
Question + Samples + Resources = Tool

## Slide 5: Question
What virus is in my sample?
  Unknown – need unbiased method
  Sequencing depth – need lots of data/sample
How is the virus evolving during an outbreak?
  Known – can use a targeted method
  Sample size – need to sequence lots of viruses
How is the virus evolving within a host?
  Known – can use a targeted method if accurate
  Sequencing depth – need lots of data/sample

## Slide 6: Samples
Target to background ratio
  Sample type and virus dependent (e.g. Zika virus in serum)
    CT values, house-keeping genes, total nucleic acid, carrier RNA?
  Determines unbiased versus targeted approach
Integrity
  RNA/DNA extraction and storage
  Determines read/amplicon lengths

## Slide 7: Resources
Money $$
  Do you have enough $$ to generate the required data?
  Determines library prep and platform
Time
  How quickly do you need the data?
  Determines platform
Environment
  Fully-equiped molecular biology lab? With personal sequencer?
  Access to a genomics core?
  In the field or other resource-limited environment?
  What capacity do you have to analyze data?
  Determines library prep and platform
Don’t be an ”Illumina Lab” just because you have a MiSeq

## Slide 8
Question + Samples + Resources = Tool
Tool = Library prep + Sequencing platform

## Slide 9: Tools – Library prep
Untargeted metagenomics
  Sequence everything
  Slightly biased additions
    Dnase treatment
    Host RNA depletion (e.g. rRNA)
Pros
  Gold standard for pathogen sequencing (limited biases)
  Do not need to know what you are looking for
Cons
  Often requires lots of data/sample to cover target
  Computationally challenging

## Slide 10: Tools – Library prep
Targeted/enriched metagenomics
  Sequence mostly target, but other stuff too
  Examples
    Spiked-primers during cDNA synthesis
    Target capture probes pre or post library prep
Pros
  Enhance target sequencing with minimal biases
  Can scale for lots of potential targets (all DENV, all flaviviruses, all viruses)
Cons
  Increases time, money, and skill of library prep

## Slide 11: Tools – Library prep
Targeted PCR amplification
  Sequence only target
  Examples
    16S for bacteria
    Overlapping multiplexed for near-complete virus genomes (PrimalSeq)
Pros
  Cheap and easy
  Scalable for generating large datasets
  Requires minimal sequencing data
Cons
  Biased amplification
  Easy to contaminate

## Slide 12: Tools – Library prep
Cell culture selection
  Enrich for virus in cells prior to standard sequencing
  Still commonly used in surveillance programs
Pros
  Broad enrichment for viruses that easily replicate in culture
  Mostly virus RNA, requires minimal sequencing data
  Cheap
Cons
  Biased virus composition (among species and intra-host populations)
  Potential for cell culture adaptations

## Slide 13: Tools – Sequencing platform
Large-Scale
  E.g., Illumina NovaSeq, HiSeq; PacBio; Nanopore PromethION
  Most data/$, but expensive per run
  Not affordable by most individual labs (genomics cores)
Mid-Scale
  E.g., Illumina MiSeq, NextSeq; Ion Torrent; Nanopore GridION
  mid data/$
  Affordable by some individual labs, requires maintenance
Portable
  E.g., Illumina iSeq; BGI DNBseq; Nanopore MinION
  Low data/$, but cheap per run
  Affordable and can be set up in many locations

## Slide 14: Tools – Sequencing platform
Platform | Expected Yield (Gb) | Seq Kit Cost | Estimated Cost/Gb
Illumina iSeq | 1 | $600 | $600.00
Illumina MiSeq | 15 | $1,625 | $108.33
Illumina HiSeq | 1500 | $6,810 | $4.54
Illumina NovaSeq | 6000 | $5,500 | $0.92
ONT MinION | 10 | $675 | $67.50
ONT GridION | 150 | $3375 | $22.50
ONT PromethION | 3800 | $19,200 | $5.05

## Slide 15: Tools – Sequencing platform
  Accurate sequencing, short reads
  Good for generating lots of data (NovaSeq)
  Expensive to run and maintain
  Uses:
    Large projects (samples in home lab)
    Accurate sequencing (intrahost, metagenomics)
Illumina
  Long reads, error prone
  Good for generating quick data
  Rugged, cheap to run (reusable flowcells)
  Uses:
    Field or limited resources
    Lab for long reads and quick data
MiSeq/NovaSeq

## Slide 16: Controls + accuracy
Controls
  Negative controls at important steps (sample collection, RNA extraction, PCR, etc)
  “Healthy” or environmental controls (metagenomics to determine background)
  Internal controls to measure efficiency of library prep and validate sequencing
  Normalize input target concentrations (important for comparing intrahost diversity)
Improving accuracy
  Dual-indexes (reduces “index” hopping)
  High-fidelity polymerases (reduces library prep errors)
  Sequence technical replicates (removes sequencing errors)
  Unique molecular identifiers (UMIs, removes sequencing errors)

## Slide 17: Scenarios
Question
  Clinical metagenomics for unknown causes of encephalitis (population study, not for diagnostics)
Samples
  Cerebral spinal fluid, maintained on cold chain
  Hundreds of samples
Resources
  Well funded clinical lab (not much NGS experience)
  Access to Genomics Core
  Not time sensitive
Tools?
Library prep
Platform

## Slide 18: Scenarios
Question
  Investigating 2019 dengue virus outbreak in Honduras
Samples
  Serum, low CTs, somewhat degraded
  Hundreds of samples
Resources
  Mobile lab
  Need data fast
Tools?
Library prep
Platform

## Slide 19: Scenarios
Question
  Evaluating Zika virus antibody escape in non-human primates (research)
Samples
  Serum, high CTs
  Dozens of samples
Resources
  Experienced, well funded molecular biology lab
  No on-site genomics core
Tools?
Library prep
Platform

## Slide 20: Scenarios
Question
  Are two mutations ~500nt apart co-occurring on the same virus genome (pilot study)?
Samples
  Cell culture supernatant, mixed infections
  Few samples
Resources
  Basic molecular lab
  Need data fast for PhD committee meeting
Tools?
Library prep
Platform

## Slide 21
  github.com/grubaughlab/path-gen_resources